## Slide 1
High Performance Data Acquisition Systems for Large Physics Experiments Anita Behere BARC

## Slide 2
Outline:
Generic requirements of DAQ for Physics Experiments
Event Acquisition System for MACE Telescope
Design approaches
Features and implementation details
Conclusion

## Slide 3
Aim of a physics experiment: Acquire signals from detectors Process the signal to extract Pulse amplitude, charge, pulse shape, time of occurrence, time of flight Collect and integrate data from all detectors Analyze and filter out unwanted events Store for later detailed analysis
Configure and control experiments
Monitor detectors/hardware to ensure safety and stability of operating parameters
Monitor data to ensure quality

## Slide 4: Common terms & definitions
Event: The complete set of signals which describe a single interaction is called an Event
Trigger: Events are random in nature, signals from a set of detectors are combined to make a decision on when an event has occurred. This is called a trigger.
  Real time detection
  Trigger efficiency - detect all events of interest and reject events which are not of interest.
Dead time: System busy time during which it can not acquire a new event is called dead-time

## Slide 5
Attribute | C&M | Experiments
Events | Regular (cycle time) | Random, Burst
Signal acquisition | Continuous | Event triggered
Data storing | Continuous | Selective
Signal bandwidth | KHz | MHz
Timings | ms | ns , us
Hardware | - | Configurable
Difference from control and monitoring DAQ systems:

## Slide 6
Few categories of DAQ for Large Physics Experiments: Accelerator based experiments Ground based Atmospheric Cerenkov experiments Neutrino experiments

## Slide 7
Ground based Atmospheric Cerenkov experiments Event Acquisition System for MACE Telescope

## Slide 8
Gamma-ray from deep space
Charge Particle
shower
Camera
Image formed by
Cerenkov event
Distribution of photon
flux on the camera
Ground Based Atmospheric Cherenkov Experiments (ACE)
- Gamma Ray telescope
~ 10 km
Energy of cosmic Gamma ray
=> Current pulse from PMT
Rise-time ~ 1-2ns
Pulse width at base ~ 6-10ns

## Slide 9
MACE Telescope, Leh, Ladakh –
Actual site photograph

## Slide 10
Camera specifications:
Wide dynamic range – 20GeV to 5TeV, 3pe to 1500pe
Acquisition of pulse profile of PMT signal of rise time ~1-2ns
Large number of camera pixels: 1088
Low event threshold – 3-5 pe => 30 to 50mV
1 KEvent/sec Event rate
Low Dead time: for better event pair resolution
Low accidental event rates at high singles rate
Control and Monitoring
Ensure safe operating conditions for PMTs: Anode current / Scalers
Ensure stable and healthy operating conditions
Challenges: High density, low power, low noise, wide band channels in compact area

## Slide 11
Non functional engineering specifications:
Remote location
Harsh Climate – 1400 ft ASL, -20 to +20 oC opearting temp
Availability : Reliability and Ease of maintenance
Self Diagnostics, graceful degradation in availability
Camera located at focal plane (25mts) of telescope
Weight and volume
Hence the designs should be simple and hardware easily accessible

## Slide 12: Implementation options for camera electronics
1. PMTs on camera. PMT signal to ground station. Entire signal processing as well as HV generation at ground station
2. PMTs along with amplifiers and laser diode modulators for transmission on the camera. Digitization at ground station
3. Entire electronics on camera, only power and communication cables to camera from ground station
Constraint: Weight, Size and Power

## Slide 13: Typical experimental setup DAQ system with CAMAC- FERA
PCI interface for
controller
PCI interface
FERA controller
CLI
GAI
PASS
Crate
Controller
ECL output bus
CONTROLBUS
PASS /
REN chain
ADCs
Crate
Controller
ECL output bus
CONTROLBUS
PASS /
REN chain
ADCs
PCI interface for
controller
PCI interface
FERA readout controller
CLI
GAI
GAI
REO
Crate
Controller
data bus
Control bus
PASS /
REN chain
ADCs
Crate
Controller
data bus
Control bus
PASS /
REN chain
ADCs
Standard buses:
CAMAC / VME / PCI

## Slide 14: TACTIC DAQ in control room
No. of Pixels for TACTIC: 349
No. of Pixels for MACE: 1088

## Slide 15: SubSystems of Event Acquisition System:
Front-end Camera Integrated modules (CIM): 68 nos., 16 channel for 1088 pixels
Backend units, 1 each:
  Data Concentrator, SBC based
  Second Level Trigger Generator, CPLD based
  Camera Controller, SBC based

## Slide 16: Block diagram of camera electronics
Data link
C&M link
IRIG-B time code
To ground
station
C&M link

## Slide 17
CIM#1
CIM
CIM
CIM
CIM
Data Concentrator
CIM#68
Data link
differential pair LVDS)
Point to Point Interconnections for event acquisition
Data archive at ground station
Gigabit ethernet
Second Level Trigger Generator
SLT
Block_SLT

## Slide 18
CIM#1
CIM
CIM
CIM
CIM
Second Level Trigger Generator
CIM#36
Trigger link
differential pair (LVDS)
Point to Point Interconnections for trigger detection
FLT group
SLT

## Slide 19: Front End Camera Integrated Module (CIM)
Sixteen pixel Front End Data Acquisition Module

## Slide 20
Front-end electronics –Camera Integrated Module (CIM) for 16 PMTs:
High Voltage,
Voltage Divider Network,
PreAmplifier,
Main amplifier,
Discriminator,
Scaler,
Local control & monitoring,
First level trigger
Camera electronics for MACE telescope

## Slide 21: Block diagram Of Camera Electronics
LVDS
Trigger Link
LVDS
Data Link
1 to 68 CIMs
Central camera Controller with Temperature and Lid Controllers
Ethernet Communication links to Control room
Time code from Master Clock in control room
Second Level Trigger generator
Main control link (I2C )
RS232 command link
Data Concentrator
SPI Status/control link

## Slide 22
Front view of Imaging Camera
HESS
MACE

## Slide 23
Rear view of imaging Camera
HESS
MACE

## Slide 24
PMT1
PMT2
PMT3
PMT576
Singles rate ~ 1MHz
Final Trigger
Stops sampling of PMT signal and starts digitization
Trigger generation time with dT jitter
dT
Coincidence
window
Trigger region of 576 pixels
Event Detection – Trigger generation

## Slide 25: Basic philosophy of trigger generation
space-time correlation among detectors in a close cluster of neighboring detectors
Apart from genuine event occurrence, all the detector channels experience random excitations due to detector dark current and background noise. There are some spurious triggers generated due to pure chance coincidence of such random excitations.
The choice of cluster size and geometry is a tradeoff between event detection efficiency and spurious trigger rejection.

## Slide 26: Chance coincidence rate expression
The chance coincidence rate (CCR) is given by
  where
  r = single channel rate for each channel (SCR)
  τ = coincidence time window
  N= Number of channels among which coincidence happens
  k = number of ways N channels can be chosen in the detector array
Optimization – low τ , low r, high N (for r*τ << N)
  to reduce the chance trigger rate
  detect all genuine events

## Slide 27: Effect of coincidence window on CCR
Shorter coincidence window helps to achieve lower chance trigger rates.
chance trigger rate of 20

## Slide 28: Effect of multiplicity on CCR
Bigger cluster size reduces the chance trigger rate
chance trigger rate of 20

## Slide 29: ACR v/s SCR and operating point for telescope for 4NN FLT 5ns, SLT 10ns
Chart: SCR (KHz)
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600
ACR limit 20 Hz | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20
CCR(4NN-Full camera) - 10 ns
CCR (Desired borders - 10 ns) | 0.003375 | 0.054 | 0.27338 | 0.864 | 2.1094 | 4.374 | 8.1034 | 13.824 | 22.1434 | 33.75 | 49.4134 | 69.984
Total 4NN combinations

## Slide 30: Trigger generation, MACE telescope – two stage, two phase pattern based coincidence
from amplifier
Photo-electron programmable threshold, pe
L0_Ch#1
L0_Ch#16
FLT
( Nearest neighbor patterns)
Discriminator
L1_CIM#1
L2_CIM#36
SLT with border resolution
FLT => ~ 5 ns SLT => ~ 8ns
Tight cluster pattern of 3 to 5 pixels at threshold ~ 3 to 5 photo-electrons
FLT
( Nearest neighbor patterns)
System wide global trigger

## Slide 31: Holding signal till trigger decision arrives:
Traditional
Analog delay (low power, low footprint)
Digital delay
Detector
FE
Analog memory
ADC
Data Buffer
Detector
FE
Digital memory
(FIFO)
Flash ADC
Event Data Buffer
Detector
FE
Cable delay
ADC / CDC
Event Readout
Trigger
Gate

## Slide 32: Event Data Flow (MACE Camera)
CIM 1
CIM 2
CIM 3
CIM 4
CIM 67
CIM 68
Data Concentrator
Central Camera Controller
Second Level Trigger Generator
Data Archiver (Server)
MACE CAMERA (Operator Console)
0
0
0
S
n
0
3
0
S
n
1
0
0
S
n
3
5
0
S
µ
5
0
0
S
µ

## Slide 33: Dead-time – loss of events when system / detector is not available
Many factors and may levels
  System busy : few us – ms
  Subsystem hang : few ms – sec
  System hang : few sec – min
  System busy for time t, for each acquired event
  Average input event rate – f1, Output event rate – f2
  Dead time = f2*t, Live time = (1- f2*t)
  f1*(1- f2*t) = f2 for random stochastic events
  f2 ~= f1 if f2*t << 1 for stochastic events
  f2 = f1 if t is just < 1/f1 for regular events
  By de-randmizing events (buffering) dead-time can be improved

## Slide 34
Event Data Flow
CIM#1
LVDS (20MBps)
Local bus (33MHz, 33MBps)
CIM#68
FIFO
FIFO
Single Board Computer (FIFO)
Data archive at ground station
Ethernet (Gbps)
FPGA: Event formatter, 8 to 32 bit converter
(FIFO)
PCI
(33MHz, 132MBps)

## Slide 35: Event flow ( Generic Timing Diagram)
Time
Initialization
Trigger Generation
Event Digitization
Event Processing
Event data transfer and Storage
Dead time of the system = t2-t1 ~50 us (Time required to digitize Region of interest)
Instead of t4-t0 ~ 500 us
Hold PMT pulse till Trigger Arrives
Raw Events Buffered in module
t1
t2
t3
t4
0
Events Buffered in DC

## Slide 36
Event formatting
Identify the event,
Identify the detector,
complete useful information with zero suppression
Format must be compact, but self documenting
Information about data quality
Include CRC to verify data integrity
Event Data volume :
Event Size = 12762 Bytes with charge for all pixels and profile only for hit pixels. Data volume at 1.6KHz ~ 20 MB/s
Transferred to archival at 1Gbps on aggregated fibre optic link

## Slide 37: Calibration system
Sky calibration - subtract the Night Sky Background (NSB) contribution while cleaning raw images.
LED Calibration to calibrate the channels in terms of relative gain
Novel event type encoded in pulse width

## Slide 38
Results: The desired performance achieved
1.6 KEvents/s with
  50us event pair resolution
  burst of 50 events
20MB/s throughput
Low trigger threshold – 3-5 pe => 30 mV
Coincidence window – 5ns & 8 ns

## Slide 39: Results: Control and monitoring
System health parameters monitored:
      Anode Current / Noise Rates / HV, Discrimination Threshold / Temperatures across modules and Camera
Safety mechanisms implemented
      PMT safety mechanism due to overexposure to light
      Camera temperature monitoring
Data integrity checks
      CRC in data
      Numbering of events
      Checks for event synchronization
      Remote configuration and control from BARC through Anunet

## Slide 40: Cherenkov Events @ MACE Camera

## Slide 41: Cherenkov Events @ MACE Camera
PMT pulse profile of events acquired in a CIM of MACE Camera (Time = 31 nS)

## Slide 42
Summary
Proprietary design in custom packaging using techniques: 1. Analog memory 2. FPGA / CPLD based trigger, event acquisition and processing in front-end modules 3. Data buffering at different stages 4. Analog – Digital mixed signal design 5. Embedded software
6. Hardware-software co-design

## Slide 43: Summary
Production with Environmental Qualification as well as ESS screening
Thermal analysis
Installation completed
Commissioning in progress
Future upgrades
  Higher sampling rate
  Higher event rate
  Other sensors for PMTs
  Trigger configuration to reduce jitter

## Slide 44
Thanks
Contribution from colleagues from Electronics Division, ApSD, CDM, BARC and ECIL