## Slide 1: Tuning Voltage Setup and Data Processing for FMCW Reflectometer
A. Amalin Prince, Department of EEE
National Symposium for Commemorating 30-years of ADITYA Tokamak,
27-28 January 2020

## Slide 2: FMCW Reflectometer: Background
Fixed Freq. for Fluctuation meas.
Swept Freq. for Density Profile
;
The reflected wave will experience a phase change a) change in path length and b) change in probing frequency
  Microwave diagnostic technique:
    Complete electron density profile (ne(r)) in the Tokamak
Notes:   is a microwave diagnostic technique which is capable of measuring the complete electron density profile (ne(r)) with minimal access requirements
  works on the principle that an em wave is totally reflected from a point in plasma where its frequency becomes equal or greater than the plasma frequency.
  microwave frequencies are reflected from various cut-off layers of the plasma which leads to measurement of the electron density profile in the tokamak.

## Slide 3: Reflectometer Setup: IPR
  Ka-band (26.5 to 40 GHz)
  Electron density
    0.875 - 1.9 e 19 m-3
  Requirements: MW source
    Wideband
    Cover wideband in short time
    Linear frequency response
Tuning Voltage Setup
  Challenges: Tuning Voltage Setup
    Nonlinear tuning voltage ramp to drive VCO linearly
    Enable easy configuration of the ramp parameters
    Multimode trigger support
    Remote configurability
  Multimode trigger unit
    Multi-trigger input sources
    Multi-trigger outputs
    Pre-trigger and post-trigger delay (1 to 4)
    Multiple modes
    Remote configurability

## Slide 4: Reflectometer: Tuning Voltage Setup
Aditya control room
Pre-trigger delay
Non linear
Ramp voltage
TON
TOFF
1
2
3
4
N
  Four modes
    Mode 0: Single trigger mode
    Mode 1: Continuous trigger mode
    Mode 2: Trigger pattern mode
    Mode 3: Continuous trigger pattern mode
Post-trigger delay

## Slide 5: Frequency Source and Its Characteristics
  For our study
    Ultrawideband VCO, (Make: SliversIMA, Model: VO4280P/01)
    Sweeping range: 13.25 to 20 GHz
Output of VCO to turning voltage.
(a) Frequency. (b) Change in frequency
Modified and unmodified tuning voltages to drive the VCO

## Slide 6: System Architecture
Hardware-Software Architecture

## Slide 7: Amplifier Circuit
High-speed op-amp driver for VCO
Simulation results of amplifier
THD versus frequency

## Slide 8: Integration
Components used
Graphical user interface
2U rack standard chassis

## Slide 9: Specifications
Trigger specifications
Ramp specifications

## Slide 10: Sample Output: Normal Mode

## Slide 11: Sample Output: Pattern Mode

## Slide 12: Characteristics of Tuning Voltage Setup
Experimental setup
Tuning Voltage Setup

## Slide 13: Characteristics of Tuning Voltage Setup
Unmodified:
200 kHz to 1400 kHz
Modified:
~30 kHz
Reduction by 40 times

## Slide 14: Comparison
Our Setup
ARG

## Slide 15: Ongoing Work: Automated Digital Signal Processing
Tuning Voltage Setup
Schematic of FMCW Reflectometry
Principle of Operation

## Slide 16: Acknowledgement
  Publications:
    Gibin C. G., Bittu N, JJU Buch, Prince A.A.*, Neena G., and Surya P, (2019) ‘Characteristics of Arbitrary Ramp Generator: A tuning voltage setup for the FMCW Reflectometer’, IEEE Transactions on Instrumentation and Measurement, DOI: 10.1109/TIM.2019.2939933 [early access].
    Gibin C. G., Abhishek M., Sriyash C., Prince A.A. *, JJU Buch, and Surya P, (2019) ‘A Novel and efficient hardware accelerator architecture for signal normalization’, Circuits, Systems & Signal Processing, DOI: https://doi.org/10.1007/s00034-019-01262-3 [early access].
    Gibin C.G., JJU Buch, Prince A.A. * and Pathak S., (2019) ‘Design of configurable multi-mode trigger unit’, Elsevier Measurement, vol. 139, pp. 482-489.
  Collaborators:
    Dr. Surya Pathak and Mr. JJU Buch, Microwave and ECE Diagnostics Division, Institute for Plasma Research, Gandhinagar.
  Funding:
    BRFST and BRNS through National Fusion Program (NFP)