## Slide 1
Overview of Data Acquisition and Central Control System of Steady state Superconducting Tokamak (SST-1)
S. Pradhan*, K. Mahajan, H. K. Gulati, M. Sharma, A. Kumar, K. Patel, H. Masand, I. Mansuri, J. Dhongde, M. Bhandarkar and H. Chudasama
Institute for Plasma Research, Gandhinagar, Gujarat, INDIA
*pradhan@ipr.res.in
10th IAEA Technical Meeting on Control, Data Acquisition and Remote Participation for Fusion Research 20-24 April 2015 at IPR India

## Slide 2
Steady State Superconducting Tokamak (SST-1)

## Slide 3
Introduction
    SST-1 Data Acquisition (DAQ) and Central Control System (CCS) Features:
    Lossless, Continuous Acquisition
    10KSPS to 1MSPS Sampling Frequency
    Distributed & Hierarchal
    Event Driven
    Controls & Monitors Remotely
    Supports Heterogeneous Sub-systems
  CCS consists of
Network Infrastructure
Control Room Infrastructure
Machine and Experiment Control
Plasma Control and Timing System,
GPS based Time Synchronization
Storage Area Network
Audio/Video Systems
  DAQ consists of
    Slow Data Acquisition Systems
    Fast Data Acquisition
    CAMAC based Systems
    PXI based Systems
    MATLAB based Data Analysis Utilities
025/P, 026/P, 027/P,030/P, 049/P, 050/P, 062/P,069/P)
023/P, 0268)

## Slide 4
Central Control System (CCS) Configuration
100Mbps Conventional
Real-time Deterministic Data transfer
Time Synchronization
Clock Synchronization

## Slide 5
Interfacing of SST-1 various Sub-Systems with MCS

## Slide 6: Plasma Control System Configuration
VME SBC
RFM
DSP
ADC
ADC
ADC
Timing Sys
VME Bus
PCI Bus
FPDP Bus
Clock
Ethernet
Realtime Data Network
Timing System Network
APC I/F
To APC Power supply
ADC : Pentek 6802, 96 (32*3) channels, 24bit, sampling 10KSPS
DSP : TSC-43, Quad Tiger-shark TS101 DSP on a PMC board having FPDP interface
RFM : VMIC 5579, Memory of 64MB, sustained link speed of 13.4 Mbytes/s
Timing system
VME Processor: SBS VG4, Processor PPC 750, 400Mhz with VxWorks 5.5 as RTOS

## Slide 7: Existing Overall PCS connectivity

## Slide 8
Horizontal Plasma Position Control Loop
Schematic way for Vertical Field(BBV ) generated & resulting force (FBV)
Schematic of BV Feedback Loop
Feedback loop uses – IP , Delta R as feedback signal and manipulated variable as IBV
Discharge starts with Feed Forward Loop
Active Feedback starts after discharge by few ms i.e. once Plasma column is completely formed
Loop time ~ 2.0ms
IBV

## Slide 9
SST-1 Timing System

## Slide 10
GPS Based Time Synchronization System

## Slide 11
SAN Based Centralized Storage System
10TB capacity

## Slide 12
Overview of SST-1 Data Acquisition System
Major Tasks
Centralized Data Acquisition for SST-1 diagnostics
Centralized Data Storage Server for Archival And Retrieval.
Data Analysis at different Network nodes (Client/Server).
Communication interface with SST-1 Central Control System.
~ 150 slow (100 KSPS) , 20 Fast (MSPS) in PXI/CAMAC platform operating now

## Slide 13
SST-1 Data Archival and Retrieval System

## Slide 14
Matlab based Data Conversion & Plotting
Data Conversion Utility
Matlab GUI Based SSTPLOT Data Plotting with various features
Plotted Data Fig

## Slide 15
Experimental Data Analysis Utility is developed in Matlab
&
Some results of recently carried out SST-1 Experiments

## Slide 17
Comparison between Magnetic Probe, Flux loop & Analytical methods for Horizontal Shift Measurement - Shot No.6065

## Slide 18
Effective edge safety factor and Grad- Shafranov parameter for shot No- 6065

## Slide 19
Data Acquisition and Control System Upgrade plan

## Slide 20
Central Control Room
Diagnostic Hall
Office Corridor
RF Bay
Computer Center
Cryo Hall
Water Cooling
Utility Building
RF Lab
NBI
APPS
Planned 10Gbps Network Architecture for SST-1
12 Core Single Mode Fiber
Core Switch
1G Access Switch
LIU
50 meter
80 meter
150 meter
300 meter
190 meter
150 meter
300 meter
300 meter
150 meter
250 meter
24 Core Single Mode Fiber
(72 Node)
(18 Node)
(18 Node)
(8 Node)
(4 Node)
(8 Node)
(8 Node)
(4 Node)
(8 Node)
(8 Node)
10G Access Switch
Patchcord
Stacking
10G User

## Slide 21
Evaluation of White Rabbit Technology using evaluation kit from Seven-solution Spain
Single solution for real-time Data transfer, Trigger and Time
Open source
Low Cost
Heterogeneous Platform support

## Slide 22
SST-1 Diagnostics DAQ Hardware Upgradation Plan
Slow Channels : Sampling rate < 100-250 KSPS
Fast Channels : Sampling rate = 1MSPS or more
Sampling Rate | Current DAQ Card | Upgrade DAQ Module | Channels Catered/ Future Plan | Current Acquisition time | Future Acq. time
1 MSPS | CAMAC 2-Ch card | PXIe 6366 | 12 / 21 | 512 ms | 4 sec
10 MSPS | N.A. | PXI 6115 | 00 / 08 | N.A. | 4 sec
10 KSPS | PXI-6071 | No change | 36 / 84 | 3 sec | Continuous mode
100 KSPS | PXI-6143 | No Change | 58 / 189 | 3 sec | Continuous mode

## Slide 23: New Proposed Configuration for PCS Hardware
Industrial PC
Multiple IO chassis configurations
Use PC based controllers
Keep separate the controllers and IO chassis
PC and IO connect with PCIe bus link
Replace/upgrade PC whenever required
MXI link

## Slide 24
Conclusion
Central Control System (CCS) is distributed, modular & scalable
Integrates all heterogeneous SST-1 subsystems
CCS is indigenously designed, developed, implemented, tested and validated for the operational since 2008.
CCS is built-on well proven technologies like
  vxWorks RTOS for deterministic control,
  VME, PXI, FPGA for hardware implementation,
  Fiber optics for network backbone,
  DSP for real-time computation &
  Reflective memory for high-speed data transfer etc.
CCS architecture is being upgraded to fulfill the today’s requirements of SST-1 using cutting edge technologies

## Slide 25: Please be welcome & find the details during the poster sessions
Sr No. | Abstract ID | Abstract Title | Author
1 | 028/P | SST-1 CAMAC based Data Acquisition System for fast plasma diagnostics and future up gradation plan | Imran Mansuri
2 | 023/P | Overview of Data Acquisition System for SST-1 Diagnostics | Manika Sharma
3 | 069/P | Overview of Time Synchronization System of Steady State Superconducting Tokamak SST-1 | Aveg Kumar
4 | 050/P | Archiving and retrieval of experimental data using SAN based centralized storage system for SST-1 | Manisha Bhandarkar
5 | 049/P | Design, architecture and operational experience of Machine Control System [MCS] for SST-1 | Harish Masand
6 | 030/P | Current status and upgrade plan for Networking System of Steady State Super conducting Tokamak SST-1 | Hitesh Gulati
7 | 027/P | SST--1 Central Control Infrastructure: An Overview | Jasraj Dhongde
8 | 025/P | Present Status and Future Plan for SST-1 Real Time Network | Kirti Mahajan
9 | 026/P | Audio Visual system for SST-1 operations | Hitesh Chudasama
10 | 062/P | Design and Architecture of SST-1 basic plasma control system | Kirit Patel
11 | 031/O | Overview of data acquisition and central control system of steady state superconducting tokamak (SST-1) | Subrata Pradhan

## Slide 26
SST-1 Existing Network (Schematic)