## Slide 1: The demonstration of Lustre in EAST data system
F.Wang1, Y.Chen1, S.Li1, F.Yang1, 3, B.J.Xiao1, 2
1Institute of Plasma Physics, Chinese Academy of Sciences, Hefei, China
2School of nuclear science and technology, University of Science and Technology of China
3Department of Computer Science , Anhui Medical University, Hefei, China

## Slide 2: OUTLINE
1. Introduction
2. System Design & Implementation
3. Test Results
4. Summary

## Slide 3: 1. Introduction
DAQ Nodes: >40
Channels: >2500
Sampling: 1Hz~60MHz
Bus: PCI/PXI/PXIe
Stream: 2GB/s
Data: 100TB (2014)
Database: MDSplus
EAST Distributed and Continuous Data Acquisition System

## Slide 4: High-speed Data Acquisition
DAQ for microwave reflectometry
  National Instruments PXIe-5122
  4 channels x 60M/s
  ~500MB/s
  ~500GB/1000s shot
DAQ for polarimeter interferometer
  National Instruments PXI-5105
  8 channels x 10M/s
  ~160MB/s
  ~160GB/1000s shot
It takes much time to access these high sampling rate data in case of long-term discharge, and the current data storage system become the bottleneck of whole data system.

## Slide 5: Data Storage System
MDSplus new shot data storage
  DELL M820 blade servers: 8
  Local raid storage: 2TB x 8
  Write data speed: 250MB/s x 8
  Network bandwidth: 10GbE x 2
MDSplus history shot data storage
  DELL MD3200 SAS Storage
  Total capacity: 300TB
  Write data speed: 300MB/s
  Network bandwidth: 10GbE x 2
The new shot data have to been moved to history shot data storage in several days;
The local data storage is not easy to manage, and consumes much CPU and RAM resources;
DELL M820
DELL MD3200

## Slide 6: Requirements
A new data storage system is necessary for the continuous data acquisition of EAST tokamak
  Duration: 1000s
  Large capacity: 500TB
  High performance: 2GB/s continuous write
  Easy to use by Linux servers
  Easy to manage data
  Online upgrade capability
  Scalability: capacity & performance
  Reliability: redundancy, raid, backup
  …

## Slide 7: OUTLINE
1. Introduction
2. System Design & Implementation
3. Test Results
4. Summary

## Slide 8: 2. System Design
System architecture of data storage system based on Lustre

## Slide 9: Lustre File System
The Lustre file system is an open-source, high performance, parallel file system that supports many requirements of leadership class HPC simulation environments.
  Performance
  Scalability
  POSIX standard compliance
  High-availability
DDN EXAScaler, is a next generation parallel file storage system appliance that combines DDN award-winning HPC storage technology with the open-source Lustre file system.
MDSplus data will be stored on the Lustre file system, and shared with computing servers.
Lustre Software Release 2.x Operations Manual

## Slide 10: System Configuration
InfiniBand 56Gbps FDR switch
DDN SFA7700: 60 x 6TB SAS drive
DDN SS8460: 84 x 6TB SAS drive
Raw capacity: 860TB
Raid Level: 8+2 raid6
Available capacity: 600TB
Lustre: DDN EXAScaler-2.1.1
I/O Server nodes: 6
  2 MDS: SUGON I620
  4 OSS: SUGON I620

## Slide 11: DDN SFA7700
DDN SFA7700 is a high performance raid for big data storage and HPC data storage.
  High performance: 10GB/s
  Active-Active RAID Controller
  Advanced Cache Optimize
  High density Expansion Enclosure
Horizontal (Scale-out)
Vertical (Scale-up)

## Slide 12: Data Flow
1. The acquired data are cached in local SSD;
2. Every 5s slice data are sent to server by TCP socket;
3. The slice data are saved into mdsplus on Lustre;
4. The shot data are synchronized to backup server;
1
2
3
4

## Slide 13: OUTLINE
1. Introduction
2. System Design & Implementation
3. Test Results
4. Summary

## Slide 14: 3. Test Results
Hardware
  Storage DDN SFA 7700 + SS8460
  MDS server SUGON I620 server ＊2
  OSS server SUGON I620 server ＊4
  Client DELL R720 server ＊4
    CPU E5-2650 v2 / 32GB RAM
Software
  OS CentOS 6.5 X64
  OFED OFED2.3
  EXAScaler 2.1.1 (Lustre 2.5.19)
Tools
  IOZONE-3-414
  MDSplus-6.1-83

## Slide 15: IOZONE Test
Client: 1, Process: 1
Client: 1, Process: 8
Client: 4, Process: 4 x 10
Client | Process | Read | Write
1 | 1 | 0.9GB/s | 1GB/s
1 | 10 | 2.8GB/s | 3.2GB/s
4 | 40 | 9.0GB/s | 10.0GB/s

## Slide 16: MDSplus Test
Client | Process | Tree | Local | Lustre
1 | 1 | 1 | 80MB/s | 120MB/s
1 | 4 | 1 | 260MB/s | 400MB/s
4 | 8 | 4 | 1500MB/s | 2000MB/s
1 mdsplus client to 1 mdsplus tree
4 mdsplus processes to 1 mdsplus tree
4 mdsplus client to 4 mdsplus tree

## Slide 17: OUTLINE
1. Introduction
2. System Design & Implementation
3. Test Results
4. Summary

## Slide 18: 4. Summary
A new data storage system based on Lustre and InfiniBand has been designed and implemented to meet the requirement of large amount of data storage for EAST;
The new data storage system has good performance and scalability, and it can be used as either mdsplus data storage or video/image data storage;
The new data storage system will be used in the next campaign of EAST tokamak experiment.

## Slide 19
Thanks for your attentions!