## Slide 1: Configuration Management for ASDEX Upgrade
Gregor Neu, Alex Gräter, Christopher J. Rapson, Gerhard Raupp, Wolfgang Treutterer, Dietrich Zasche, Thomas Zehetbauer and the ASDEX Upgrade Team
Max-Planck-Institut für Plasmaphysik
Boltzmannstrasse 2, 85748 Garching, Germany

## Slide 2: A child’s dream …
http://fc-foto.de/30777310

## Slide 3: An youngster’s dream …
http://www.digitaltrends.com/mobile/faa-orders-airlines-to-replace-cockpit-displays-in-1300-jets-over-wi-fi-interference/

## Slide 4: A man’s dream
http://cdn.bmwblog.com/wp-content/uploads/bmw-active-cruise-control-1.jpg

## Slide 5: A fusion researcher’s dream ?

## Slide 6: A CODAC officer’s nightmare
pellet material,size, speed, frequency
ECRH gyrotron cathode voltage, frequency, temperature, polarisation angle,, poloidal/toroidal mirror angle
ICRH frequency, power, generator voltage, line terminating tuning, arc detection threshold, recovery time
NBI gas species, power, source priority, acceleration voltage, beam inclination angle, beam focussing voltage, pre-vaccum
Power supply voltages, current limits, controller gains, flywheel generator speed
Midplane manipulator injection/extraction positions, speed, temperature threshold
Cooling water pressure, temperature, valve settings
thyristor firing angle characteristics, crowbar resistivities/triggering thresholds
Coil current limits, force limits, max. temperature, max. strain
DCN Laser Interferometer LOS geometry, filtering, optical correction
ECE frequencies
Toroidal field
Flattop plasma current
Planned triangularity
Main/divertor chamber gas valve/species mapping, flow characteristics
Locked mode alarm threshold
Detachment alarm threshold
Magnetic pickup coil sensitivities
NBI gas species, power, source priority, acceleration voltage, beam inclination angle, beam focussing voltage, pre-vaccum
ICRH frequency, power, generator voltage, line terminating tuning, arc detection threshold, recovery time
ECRH gyrotron cathode voltage, frequency, temperature, polarisation angle,, poloidal/toroidal mirror angle
Perturbation coils patch panel setting, voltage, polarity, frequency
Controller algorithms, mode transition policy, gains, input signals, actuator choices, output clipping limits, control error monitor
All these parameters
must be set prior to operation
change never, occasionally, or in each discharge
How ???
can be dependent on others
need to be checked for correctness and consistency

## Slide 7: Overview
What is configuration (management) ?
The ideal way ...
  ... and why it won´t work
The practice on ASDEX Upgrade ...
  ... not ideal, but working
  Types of configuration data
  Tools for managing the configuration process
  Policies to manage experiment evolution and parameter dependencies
Notes: Experiment: operation space
Reactor: Operation point
Physics scenario: (defined here as a time-ordered set of target equilibria and time sequences of other plasma states that define an intended discharge history over time)
Control scenario: (defined here as the actuator waveforms needed to produce the physics scenario, as well as the definition of control algorithms used at specific times during the discharge)
Configuration are the parameters in a system that make it perform in the desired way
Limited resources: if systems could always provide their full range of functionalities (unlimited resources) there would be no need to configure them!
range of plant functionality is provided by plant system hardware/firmware (by plant system designers)
applicable functionality is defined and specifics tuned by set parameters (plant system operators)
Diagnostic channels
Heating

## Slide 8: General task : General solution ?
General task: Provide a complete and consistent set of parameters
Various similar approaches
  JET: Level 1
  DIII-D: Pulse Schedule File
  W7-X: Experiment Program
  ASDEX Upgrade: Discharge Program
  ITER: Pulse Schedule
  ...
many similarities / many differences
in content and generation workflow
-
depending on system scope, operation procedures / responsibilities, ...
Notes: Experiment: operation space
Reactor: Operation point
Physics scenario: (defined here as a time-ordered set of target equilibria and time sequences of other plasma states that define an intended discharge history over time)
Control scenario: (defined here as the actuator waveforms needed to produce the physics scenario, as well as the definition of control algorithms used at specific times during the discharge)
Configuration are the parameters in a system that make it perform in the desired way
Limited resources: if systems could always provide their full range of functionalities (unlimited resources) there would be no need to configure them!
range of plant functionality is provided by plant system hardware/firmware (by plant system designers)
applicable functionality is defined and specifics tuned by set parameters (plant system operators)
Diagnostic channels
Heating

## Slide 9: Example: ITER Pulse Schedule
operational
limits
Pulse metadata, e. g. pulse number, physics goal, type of pulse etc.
Campaign info
Segment 1
Segment 2
Segment 3
Segment 4
Segment n
PCS configuration
ECH
ICH
NBI
CPSS
Plant Sys N
Diag 1
Diag N
Cryo
Level 1:
Level 2:
Level 3:
Level 4:
"Pulse schedule composed of building blocks"
Courtesy A. Winter
Configuration objects for necessary plant systems
Contains the configuration data which remains constant during a pulse or will change event based, e.g. two sets of configuration parameters which may depend on an event to trigger change
metadata such as operational limits, pulse number, physics goal, audit trail etc.
all necessary pulse control waveforms/parameters/etc (segmented)
PCS configuration (algorithms and architecture, not parameters)
Notes: Level 0: configuration objects for necessary plant systems
  Contains the configuration data which remains constant during a pulse or will change event based, e.g. two sets of configuration parameters which may depend on an event to trigger change
  CPSS (coil power supply system)
Level 1: PCS configuration (algorithms and architecture, not parameters)  RTF config schema
Level 2: segment information with all necessary parameters/waveforms/etc.
Level 3: metadata such as operational limits, pulse number, physics goal, audit trail etc.
Pulse schedule composed of building blocks

## Slide 10: The Ideal Way to Configure Experiments ...
Actuator Systems
Diagnos. Systems
Plasma Control
Execution
Defining the configuration for a specific pulse is a process
9

## Slide 11: The Ideal Way to Configure Experiments ...
Defining the configuration for a specific pulse is a process :
Describe an idea with key parameters.
Express in physics quantities.
Translate into control relevant quantities
Detail required technical settings
  engineering aspects
  machine parameters
Each level is an abstraction
  Keep focus on relevant parameters
  Hide implementation details
10
Plant and Control Systems Settings
controller characteristics
plant system characteristics
Experiment Desc.
physics model
Physics Waveforms
Control Waveforms
Plant Sys. Configuration
Control Configuration
Actuator Systems
Diagnos. Systems
Plasma Control
Idea
Execution
Experiment Proposal
idea description
key plasma states
technical parameters
physics model
control model
engineering model
Physics Scenario
plasma regime description
evolution of major plasma quantities
Control Scenario
choice of control functions
evolution of controlled technical (FF) / physical (FB) quantities

## Slide 12: ... only exists in theory (1): Ambiguity challenge
physics model
physics model
physics model
physics model
physics model
physics model
Plant and Control Systems Settings
controller characteristics
plant system characteristics
Experiment Desc.
physics model
physics model
Physics Waveforms
Physics Waveforms
Control Waveforms
Control Waveforms
Control Waveforms
Plant Sys. Configuration
Control Configuration
Plant Sys. Configuration
Control Configuration
Plant Sys. Configuration
Control Configuration
Control Configuration
Plant Sys. Configuration
Control Configuration
Actuator Systems
Diagnos. Systems
Plasma Control
Idea
Execution
Multiple transformation options
Boundary conditions narrow the variety of choices
  Operation windows
  Parameter dependencies
No guaranteed unique solution  additional soft requirements
  Model/plant optimization aspects
  Experience and intuition
  Operational state of plant
  Resilience: mimimize changes
1 > k
k > m
m > n
Experiment Proposal
idea description
key plasma states
technical parameters
physics model
control model
engineering model
11
Physics Scenario
plasma regime description
evolution of major plasma quantities
Control Scenario
choice of control functions
evolution of controlled technical (FF) / physical (FB) quantities

## Slide 13: ... only exists in theory (2): Dependency challenge
Plant and Control Systems Settings
controller characteristics
plant system characteristics
Experiment Desc.
physics model
Physics Waveforms
Control Waveforms
Plant Sys. Configuration
Control Configuration
Actuator Systems
Diagnos. Systems
Plasma Control
Idea
Execution
Experiment Proposal
idea description
key plasma states
technical parameters
physics model
control model
engineering model
12
Physics Scenario
plasma regime description
evolution of major plasma quantities
Control Scenario
choice of control functions
evolution of controlled technical (FF) / physical (FB) quantities
Coil Current Machine Limit
Power Supply Current Limit
Coil Current Protection Limit
Coil Current Operation Limit
Coil Current Command Limit
Coil Suspension Force Limit
Plasma Shape Constraint
Exp. Goal Constraint
Iteration loops : Typical optimization problem with side-conditions

## Slide 14: ... only exists in theory (3): Evolution challenge
Plant and Control Systems Settings
controller characteristics
plant system characteristics
Experiment Desc.
Physics Waveforms
Physics Waveforms
Control Waveforms
Control Waveforms
Control Waveforms
Plant Sys. Configuration
Control Configuration
Plant Sys. Configuration
Control Configuration
Plant Sys. Configuration
Control Configuration
Control Configuration
Plant Sys. Configuration
Control Configuration
Actuator Systems
Diagnos. Systems
Plasma Control
Idea
Execution
Sources of evolution
  Better physics understanding  refined physics model
  Smarter controllers  more/different waveforms  changed parameter set
  Plant system upgrade (actuator/diagnostic)  new settings
Each evolutionary modification
  introduces or obsoletes configuration parameters
  may change parameter dependencies
Experiment Proposal
idea description
key plasma states
technical parameters
physics model
control model
engineering model
13
Physics Scenario
plasma regime description
evolution of major plasma quantities
Control Scenario
choice of control functions
evolution of controlled technical (FF) / physical (FB) quantities
physics model

## Slide 15: ... only exists in theory (4): Human challenge
Plant and Control Systems Settings
controller characteristics
plant system characteristics
Experiment Desc.
physics model
Physics Waveforms
Control Waveforms
Plant Sys. Configuration
Control Configuration
Actuator Systems
Diagnos. Systems
Plasma Control
Idea
Execution
Men-in-the-loop
  Human experience and intuition substituted(s) missing models
  Plant operators responsible for safety want to retain authority on plant settings
  … communicate orally  risk of misunderstanding
  … edit parts of configuration concurrently  risk of inconsistency
Experiment Proposal
idea description
key plasma states
technical parameters
physics model
control model
engineering model
14
Physics Scenario
plasma regime description
evolution of major plasma quantities
Control Scenario
choice of control functions
evolution of controlled technical (FF) / physical (FB) quantities

## Slide 16: ASDEX Upgrade: Types of configuration data
Shot Request Database
  key plasma and plant parameters
  links to experiment proposal
  links to executed discharges
Discharge Program
  waveforms for
    control methods
    control references
    actuator feedforward commands
  segmented structure
    transition rules for segments
Plasma Control System Release
  supported control algorithms
  process descriptors
  I/O descriptors
Plant Systems Recipes
  ready-made named sets of consistent plant parameters
15
Control System Release
+ process descriptors
Shot Request DB
Plant System Recipes
global base parameters + local tuning parameters
Plant / Control Settings
Experiment Proposal
Physics Scenario
Control Scenario
Discharge Program (DP)
segmented
Notes: DP must be consistent with provided resources.

## Slide 17: ASDEX Upgrade: Configuration management tools
16
Wiki
ShapeDesign, ASTRA, Simulink models
DP Editor
Discharge Program (DP)
segmented
Control System Release
+ process descriptors
Shot Request DB
Plant System Recipes
global base parameters + local tuning parameters
Plant / Control Settings
Experiment Proposal
Physics Scenario
Control Scenario
Supervisory plant system
Parameter Server
Flight Simulator (planned)
Modeling
Simulation
Verification
Dependency rules Verification
Distribution
Automatization
User Interface
Planning
Plant gateway
Visualisation
Notes: DP must be consistent with provided resources.

## Slide 18: Discharge Program Editor
DP
repository
Parameter Server
Control mode descriptors
Selected control settings Selected plant settings
Previous discharges
Standard segments
Exception handling rules
Signal
property DB
Ranges Units
Bitgroups
Signal waveforms organised in segments
Table and plot panes
Dedicated control task views
User views with custom waveform selection
Waveform out-of-bound visualisation
DP comparison
Editor for dedicated control parameters

## Slide 19: Managing Discharge Program Evolution
Discharge Program contains
  Integral segments
    dedicated exploratory pulse phases (e.g. plasma phase)
  Linked segments
    standardized phases (e.g. pre-/post plasma or ramp-down phases)
    provided in a separate repository
    links are resolved in final pulse preparation step
Evolution policies
  Pulse-specific changes  integral segments
  Context-related changes  linked segments
  Incremental changes enabled by version control
    Store Discharge Programs and Standard Segments
    Re-use stored Discharge Programs as templates for new pulse setups
18
Discharge Program (DP)
segmented
repository of standard segments
link
provide
Notes: DP must be consistent with provided resources.

## Slide 20: Parameter Server
Connects a multitude of parameter sources to applications (databases, PLC, conf. files)
Provides consistency for dependent parameters (clipping limits – operation limits)
Parameter Server
Eval-uator
Eval-uator
Eval-uator
Con-troller
Con-troller
Con-troller
Actuator
Actuator
Eval-uator
Reference Generator
Segment Scheduler
xml
xml
xml
xml
xml
DB
xml
xml
xml
xml
xml
xml
xml
xml
Pulse Schedule
Parameter Database
PLC (S7) settings

## Slide 21: Managing Parameter Dependencies
Parameter service
  Web-service interface for client connection
  Parameter values are looked up or computed on demand
  Parameter definitions read from resources into layers
    Start-up layer (built-in parameters, mostly for self-administration)
    Initialization layer (default settings from parameter “database” XML files)
    DP layer (optional pulse-dependent parameter variants)
    Application layer (e.g. settings defined contributed by real-time diagnostics)
  Parameter values defined in DP or Application layer take precedence
Parameter object types
  Value parameters  stored data (name/value pair)
  Access parameters  fetch data from external source
  Function parameters  rule-based computation (Ruby)
    Derived parameters
    Parameter verification and consistency checks

## Slide 22: Summary
Configuration management is a complex optimization process
Parameter dependencies, system evolution and configuration consistence pose major challenges
Main pillars of ASDEX Upgrade configuration management
  Discharge Program Editor
    processes waveforms and pulse-specific parameters
    supports to re-use standard segments and previous Discharge Programs
  Parameter Server
    resolves parameter dependencies
    provides consistency checks
  Flight Simulator (planned)
    verifies the mapping of experiment goals to control and machine parameters
Process automation based on these tools is on-going
Better tool integration shall improve future user experience

## Slide 23: Summary
Configuration management is a complex optimization process
Parameter dependencies, system evolution and configuration consistence pose major challenges
Main pillars of ASDEX Upgrade configuration management
  Discharge Program Editor
    processes waveforms and pulse-specific parameters
    supports to re-use standard segments and previous Discharge Programs
  Parameter Server
    resolves parameter dependencies
    provides consistency checks
  Flight Simulator (planned)
    verifies the mapping of experiment goals to control and machine parameters
Process automation based on these tools is ongoing
Better tool integration shall improve future user experience
pellet material,size, speed, frequency
ECRH gyrotron cathode voltage, frequency, temperature, polarisation angle,, poloidal/toroidal mirror angle
ICRH frequency, power, generator voltage, line terminating tuning, arc detection threshold, recovery time
NBI gas species, power, source priority, acceleration voltage, beam inclination angle, beam focussing voltage, pre-vaccum
Power supply voltages, current limits, controller gains, flywheel generator speed
Midplane manipulator injection/extraction positions, speed, temperature threshold
Cooling water pressure, temperature, valve settings
thyristor firing angle characteristics, crowbar resistivities/triggering thresholds
Coil current limits, force limits, max. temperature, max. strain
ECE frequencies
Toroidal field
Flattop plasma current
Planned triangularity
Main/divertor chamber gas valve/species mapping, flow characteristics
Locked mode alarm threshold
Detachment alarm threshold
Magnetic pickup coil sensitivities
ICRH frequency, power, generator voltage, line terminating tuning, arc detection threshold, recovery time
ECRH gyrotron cathode voltage, frequency, temperature, polarisation angle,, poloidal/toroidal mirror angle
Perturbation coils patch panel setting, voltage, polarity, frequency
All these parameters
must be set prior to operation
change never, occasionally, or in each discharge
How ???
can be dependent on others
need to be checked for correctness and consistency