## Slide 1: The implementation of a data acquisition and service system based on HDF5 and EPICS
Y.Chen1, B.J.Xiao1, 2, F.Wang1, S.Li1, F.Yang1, 3
1Institute of Plasma Physics, Chinese Academy of Sciences, Hefei, China
2School of nuclear science and technology, University of Science and Technology of China 3.Department of Computer Science , Anhui Medical University, China

## Slide 2: OUTLINE
Introduction
System Architecture
Implementation
Conclusion

## Slide 3: Introduction
KTX(Keda Torus for eXperiment) is a new Reversed Field Pinch (RFP) magnetic confinement device which is located at University of Science and Technology of China (USTC). It is designed by ASIPP and USTC.[1]
[1]. Wandong Liu, Wenzhe Mao, Hong Li, et al, Progress of the Keda Torus eXperiment Project in China: design and mission, Plasma Phys. Control. Fusion56(2014) 094009.

## Slide 4: Introduction
This system is a data system containing data acquisition, data acquisition control, data storage and data service. It adopts HDF5 as its low-level data storage format.
Requirements
Shot ~100ms
~2000 channels
Sampling rates: 250KS/s to 10 MS/s
Communicate with central control system
Easy to access data after each shot

## Slide 5: HDF5 and EPICS
HDF5 [2]
HDF5 is a data model, library, and file format for storing and managing data. It has been used worldwide in many scientific research field.
EPICS [3]
EPICS is a set of Open Source software tools, libraries and applications developed collaboratively. It has been used worldwide to create distributed soft real-time control systems for scientific instruments.
[2] HDF Group, http://www.hdfgroup.org/HDF5/
[3] EPICS, http://www.aps.anl.gov/epics

## Slide 6: OUTLINE
Introduction
System Architecture
Implementation
Conclusion

## Slide 7: System Architecture
The data system includes data acquisition control, data acquisition, data storage and data service. So according to the function, it can be divided into four components:
Data Acquisition Console
DAQ Nodes
Data Archive System
Data Service

## Slide 8: System Architecture
Data Acquisition Console
Data Access Clients
Central Control System
Administrator
Users
Data Archive System
Data Service Server
DAQ nodes
Data Pool
request
request
data
request
request
data
response
response
request

## Slide 9: OUTLINE
Introduction
System Architecture
Implementation
Conclusion

## Slide 10: Data Acquisition Console
The data acquisition console is considered as a middleware between Central Control System (CCS) and DAQ nodes, and is responsible for transferring the commands from CCS to DAQ nodes and the status from DAQ nodes to CCS.
It includes two functions.
DAQ Management
monitors DAQ status and sets DAQ parameters.
DAQ Flow Control
controls the data acquisition flow.

## Slide 11: DAQ Management
DAQ Status Monitor
DAQ Parameter Setting
DAQ Parameter
DAQ Flow Control
DAQ Status
DAQ Status
DAQ Parameter

## Slide 12: DAQ flow control
DAQ Flow Control
5、Reply DAQ finish status to Central Control System after all DAQ nodes have finished data acquisition successfully.
DAQ Parameter
Central Control System
DAQ nodes
Data Archive System
DAQ Status
(1)Shot Command
(2)Shot Command
(5) finish status
(3)Parameter
(5)finish
1、Receiving Shot Command from Central Control System when new discharge coming.
2、Sending Shot Command to Data Archive System.
3、Sending DAQ Parameter to each DAQ node.
4、Sending Stop Command if receiving Stop Command from Central Control System .
(4) STOP
(4) STOP

## Slide 13: DAQ flow control
EPICS will be used:
Communication between DAQ flow control and Central Control System with EPCIS.
Monitoring each DAQ nodes status via EPICS.
Central Control System
DAQ flow control
DAQ nodes

## Slide 15: DAQ Nodes
The DAQ nodes are responsible for acquiring diagnostic signals. It supports continuous data acquisition with different sampling rates which is divided into low and high level. It also supports long-pulse discharge.
The hardware includes signal condition device and data acquisition computer. Different sampling rates decide different data acquisition computer.
The software structure includes four kinds of threads.
Main Thread
DAQ Main Thread
DAQ Thread
Process Thread

## Slide 16: Signal Condition
The integrator system is developed by the EAST team.
Parameters: (1) Drift: 100 s drift < 0.1 mWb ( gain=1) (2) Gain: 0.5, 1, 2, 5 (3) Output Voltage Range: -10V～+10V
The gain-variable amplifier is developed by the EAST team.
Parameters:
(1) Gains: 0.1, 0.5, 1, 2, 5, 10, 20, 50 (2) -3dB bandwidth: 500 kHz when gain=1 (3) Noise: less than 10 mV when gain=1 (4) Output range: -10 V to +10V
Gain-variable amplifier
Integrator system
Notes: （1）100s的积分飘移小于0.1毫韦伯
也可以用mVs

## Slide 17: DAQ Hardware
PXI-2022：
PXI specification Rev 2.2 compliant
16-CH differential analog inputs
Multiple cards synchronization through PXI trigger bus
16-bit A/D resolution
Bipolar analog input
Onboard 8 K-sample (16 KB) memory for data storage
4-CH TTL digital input/output
250KS/s
PXIe-6368
6 simultaneously sampled channels
16-bit vertical resolution
2 MS/s real-time sampling rate
PXIe-5105
8 simultaneously sampled channels
12-bit vertical resolution
60 MS/s real-time sampling rate
60 MHz analog bandwidth
Deep onboard memory up to 512 MB for long acquisition times
>= 1MS/s

## Slide 18: DAQ Software
Main Thread
Commands
DAQ Main Thread
DAQ Thread
Process Thread
Binary data files
Data Archive System
data
data
data
CentOS 6 / gcc
Windows / LabVIEW

## Slide 19: Data Archive System
All experimental data will be remotely transferred to the data archive system. It adopts HDF5 as its low-level data storage format.
Server：DELL PowerEdge R730
  CPU: 2 X Intel Xeon E5-2609v3
  RAM: 16GB 1600MHz RDIMM
  Disk: 8 X 4TB 7.2Kr/S NL-SAS，RAID5
  RAID controller: PERC H730P
  Network: 4 X Gigabit Ethernet
  OS: CentOS release 6.6 (Final)
  Development environment : gcc

## Slide 20: Server
Main Thread
Server Thread
data
File Operation
Other Operation
Data Operation
HDF5
Data pool
DAQ nodes
data
Operation
command
Data Acquisition Console
CentOS 6 / gcc

## Slide 21: Data Service
HDF5
Data Pool
Server Thread
Analysis and Access Thread
Main Thread
Client Plug-in
Client Interface
WebScope
Matlab
request
data
request
data
request
data
data
Data
Server
Client
Users can get data service via Client/Server or Brower/Server.

## Slide 22: Data Service
A plug-in (by gcc) for WebScope (a web data analysis and visualization tool for EAST) has been developed to view HDF5 data. Users can view all data or part of data.
Sampling rate:100KS/s, acquisition time:50ms

## Slide 23: Data Service
A plug-in (by Visual C++) for MATLAB has been developed to access the data via the Data Service interface. Users can get all data or part of data.
Sampling rate:100KS/s, acquisition time:50ms

## Slide 24: OUTLINE
Introduction
System Architecture
Implementation
Conclusion

## Slide 25: Conclusion
A data acquisition and service system has been designed and implemented based on HDF5 and EPICS for KTX.
The data system can deal with different diagnostic acquisition requirement and the DAQ nodes are easily extensible.
Users can access experiment data via Client/Server or Brower/Server.
Distributed and parallel data service function will be developed in the future.

## Slide 26
Thanks for your attentions!