## Slide 1
Controlling Plasma Disruptions and Runaway Electrons using novel techniques in Tokamak ADITYA
by
Joydeep Ghosh
Institute for Plasma Research, India
(Contribution from ADITYA Team)

## Slide 2
Disruptions in Tokamaks:
An abrupt termination of a tokamak discharge
Leading to the sudden loss of plasma stored energies
The force and heat loads, induced by disruption, damages the machine walls, support structure and in-vessel components
Runaway Electrons (RE) in Tokamaks:
Electrons that run away in velocity space due to driving force, eE, which overcomes the collisional drag force
RE generation with higher energies of several tens of MeV is expected during major disruptions in ITER
When locally deposited these REs can damage the first wall components
Introduction and Outline

## Slide 3
Both these topics of utmost importance to bigger Tokamak have been addressed in ADITYA using new techniques
Introduction and Outline
Disruptions must be avoided
and
Runaway electrons should be mitigated
The talk is organized as follows:
Novel approaches towards disruption Avoidance in ADITYA tokamak
Runaway electron mitigation in ADITYA tokamak
Summary

## Slide 4
Machine Parameters:
Major Radius: 0.75 m
Minor Radius: 0.25 m
Toroidal field: 0.75 – 1.2 T
Peak loop voltage: 20 V
Circular Plasma with circular poloidal limiter
Aditya tokamak is a mid-sized air-core tokamak
ADITYA Tokamak
Plasma Parameters:
IP ~ 70 – 160 kA
~ 1 – 4 x 1019 m-3
Te ~ 300 – 700 eV
Duration ~ 90 – 250 ms
Typical discharges of ADITYA tokamak

## Slide 5
Disruptions in ADITYA
Majority (> 95 %) of disruptions in Aditya show
MHD growth prior to disruptions
(Identified as m/n = 2/1, 3/1 resistive tearing modes)
Cessation of mode rotations and locking
Growth of neighbouring chains of islands lead to loss of confinement
Total termination of plasma current
Disruption can be induced by controlled gas puffing
Edge cooling leading to generation of resistive tearing modes
Causing Disruptions
Deliberate disruption by Gas puffing

## Slide 6
ELECTRODE
Disruption Mitigation by Biased Electrode
Capacitor Bank
Electrode Current
Plasma
Vacuum Vessel
Limiter
Flexible
bellow
Gate Valve
SCR
Ceramic
Electrode
High Field Side
Vbias
Material: Molybdenum
Diameter: 5 mm
Tip position inside limiter ~ 3 cm (near qedge ~ 3)
Exposed length ~ 2 cm
Experimental Set-up
Hence, MHD generated disruptions in Aditya tokamak are targeted with sheared rotation induced by biased electrode
Biased Electrodes induces sheared radial electric fields
Generation of sheared poloidal rotations in edge region
Sheared rotations are known to suppress the MHD fluctuation

## Slide 7
Disrupted Shot # 26570 without bias – in Black
Disruption avoided in Shot # 26571 with bias (~190V) – in Red
By applying bias voltage
Current quench avoided
Plasma current sustained
Density Restored
Temperature Restored
Stored energy Restored
Gas Puff Pulse
Bias Voltage
Bias Current
SXR emission Restored
DISRUPTION AVOIDED!!!
Bias applied
Gas puff applied
Disruption Mitigation by Biased Electrode

## Slide 8
Modes do NOT grow
Shot # 26714 without bias – Disrupted (Black)
Shot # 26719 with bias (~ 220V) - Disruption avoided (Red)
MHD Oscillations increases with gas puff in Disruptive discharge
With Gas puffing at t ~ 42 ms
With Application of bias at t ~ 41 ms
Growth of m/n = 2/1, 3/1 modes
Mode rotation ceases
And Disruption does NOT occur !!!
Mode rotation continues
Disruption Mitigation by Biased Electrode

## Slide 9
9
With Application of bias voltage
Plasma Potential profile gets modified and Radial Electric field Er and its shear increases
rotation and its shear
Leading to
As the bias voltage is increased
Increased poloidal flow shear stabilizes both m/n = 2/1, 3/1 modes
Saturated island width and stability index Δ́a decreases slowly with increase in poloidal flow shear
For bias voltage ≥ 180 Volts, the flow shear ( magnetic shear
TM generated due to gas puff are stabilized and the Disruptions caused by these modes are mitigated
Disruption Mitigation by Biased Electrode

## Slide 10
Disruption Mitigation by ICRH Power
Power Injected
~ 50 to 70 kW
5 ms prior to gas puff injection
Disruptions induced by hydrogen gas puffing are successfully mitigated by applying ICRH power through a fast wave antenna
Pre-Programmed ICRH power for disruption mitigation
Disrupted shots
A biased electrode cannot be put in the edge region of a reactor grade tokamak
Current quench avoided
Plasma current sustained
DISRUPTION AVOIDED!!!

## Slide 11
Gas-puff induced Hα intensity increase is used as a precursor for triggering the ICR pulse.
Similar to bias experiments
The plasma density is restored
Temperature is restored
disruption avoided with ICR pulse
Disruption Mitigation in Real time
Disruption Mitigation by ICRH Power

## Slide 12
Further Analysis Show
The MHD activity induced by gas puff gets reduced with ICRH pulse.
The disruption avoidance is observed with ~50 to 70 kW of ICR power
Increasing the power  70 kW does not lead to disruption avoidance
Possible Cause
The disruption avoidance does not seem to be due to heating near the Islands. ICR Heating required power > 100 kW
ICR induced radial electric field generating a shear rotation and subsequent avoidance of disruption as in case of biasing may be a possibility
Radial Electric Field measurements in presence of ICR pulse is underway
Disruption Mitigation by ICRH Power

## Slide 13
Runaway Electrons Mitigation
Mitigation techniques used in other tokamaks:
injection of high pressure gas jet through the nozzle or fast valves
Resonant magnetic perturbation (RMP) for runaway losses through magnetic fluctuation
LVF setup
Application of a short localized vertical field perturbation of 150 to 260 Gauss
The perturbation causes no disruption of the thermal component of the plasma
The perturbation leads to a radial diffusion
particle velocity along magnetic field, B
perturbation magnetic field
L Scale length of the perturbation field gradient
As the runaway particle diffusion
must be larger than the thermal particle diffusion by at least a factor of
Hence REs can be extracted without disturbing the thermal plasma
In Aditya tokamak, Localized Vertical Magnetic field (LVF) perturbation technique is successfully attempted to mitigate REs

## Slide 14
RE Extraction by LVF Perturbation
RE mitigation with application of LVF in different phases of plasma current
Results:
Significant reduction (~ 5 times) in initial RE population
Reduction in REs during current ramp up and disruption phases
Runaway current contribution in main current reduced and the discharge parameters are also improved
Breakdown phase
Current ramp up phase
Disruption phase

## Slide 15
Conclusions
Disruptions, induced by hydrogen gas puffing are successfully mitigated using biased electrode and ICR pulse techniques
Both methods show identical characteristics such as MHD activity suppression leading to disruption avoidance.
Biasing voltage ~ 180 – 250 V and ICR power of 50 – 70 kW required for disruption avoidance
Induced poloidal rotation shear > magnetic shear with biasing stabilizes the resistive tearing modes leading to disruption avoidance
ICR induced radial electric field may be inducing sheared poloidal rotation leading to disruption avoidance
The runaway electrons (RE) are mitigated using local vertical field perturbation
The REs are mitigated during plasma current startup, plasma current flattop and discharge termination phases

## Slide 16
Thank you!
The ADITYA Team:
R.Tanna, Pintu kumar, K. A. Jadeja, K. M. Patel, Nilesh Patel, K.S. Acharya, S. B. Bhatt, K.S. Shah, M.N. Makawana, C.N. Gupta, M. B. Kalal, D. S. Varia, V. K. Panchal, N. C. Patel, C. Chavda, A. Amardas, D. Sangwan, Harshita Raj, P. K. Chattopadhyay, K. Sathyanarayana, S. K. Jha, D. Raju, M.V. Gopalkrishna, K. Tahiliani, R. Jha, S. Purohit, J. V. Raval, Asim Kumar Chattopadhyay, Y. S. Joisa, C.V.S. Rao, Umesh Nagora, P. K. Atrey, S.K. Pathak, N. Virani, N. Ramaiya, S. Banerjee, M. B. Chowdhuri, R. Manchanda, Kiran Patel, J. Thomas, Ajai Kumar, Vinay Kumar, P. Vasu, J. Govindrajan, S. Gupta, Kumar Ajay, S. Pandya, K. Mahavar, M. Gupta, Praveenlal E.V, Minsha Shah, Praveena Kumari, R. Rajpal, S. V. Kulkarni & ICRH Group, B. K. Shukla & ECRH Group, P.K. Sharma & LHCD Group, R. Goswami, R. Srinivasan, I Bandyopadhyay, R.P. Bhattacharyay, Amit Sircar, N. Ramasubramanian, H. D. Pujara, H.A. Pathak, A. Vardharajalu, A. Das, S.P. Deshpande, K.K. Jain, Prabhat Ranjan, D. C. Reddy, D. Bora, Y. C. Saxena, S. K. Mattoo, A. Sen, P. I. John and P. K. Kaw.

## Slide 17
Back up slides

## Slide 18
Plasma biasing by non-resonant ponderomotive
forces of radio-frequency waves
By R. VAN NIEUWENHOVE,f V. PETRZILKAJ
AND J. A. TATARONIS§
Association Euratom-Etat Beige, Departement de Physique Statistique et Plasmas,
CP 231, Universite Libre de Bruxelles, Campus Plaine, 1050 Bruxelles, Belgium
(Received 12 December 1994)
A numerical code that computes stationary radial electric fields EOr induced by ponderomotive forces of radio-frequency waves is developed. The computed value of EOr is typically several hundred volts per centimetre when the wave frequency is 1 % lower or higher than the ion-cyclotron frequency. This value of EOr suggests that the ponderomotively induced electric field would be an effective bias in tokamaks. Numerical data are presented to illustrate the properties of this bias field.

## Slide 19
rotation (in ion-diamagnetic drift
direction) of plasma at r ~ 24 cm increases from ~ 3.5 km/s (without bias)
to ~ 7.0 km/s (with +210 V bias)
Increased Poloidal Flow Shear with Bias
Plasma Poloidal Rotation with and without biasing
Radial profiles of
(a) plasma potential
(b) radial electric field
(c) poloidal flow velocity
(d) normalised poloidal flow Shear

## Slide 20
is Spitzer resistivity
WS is saturation island width
Using Rutherford equation:
Stability index calculation from Mirnov Coil Measurements
Using
is resistive diffusion time
Alfven transit time

## Slide 21
Variation of saturation island width (WS)
and (Δ’a ) as a function of poloidal flow
shear for m = 2 and m = 3 modes.
Disruptions Avoided for
When
Ratio of Flow Shear to Magnetic Shear