## Slide 1: Overview and implementation concepts of configuration, supervision and real-time control system of ITER
A. Winter, B. Bauvir, G. Neu, A. Neto, A. V. Stephen, W. Treutterer

## Slide 2: Overview
Scheduling and configuration
Supervision
Real-time applications
  How to deal with the diagnostic measurements
  Plasma control

## Slide 3: Data flow during operation
global

## Slide 4: Stakeholder analysis and requirements
Physics expert:
  Must be able to validate a pulse (long-term) before execution, both for physics feasibility AND executability (i.e. can the machine take the demand, are all plant systems foreseen to be there etc.)
  Wants to specify pulse specific data (typically control functions, setpoints, waveforms etc.)
  Will typically specify physics quantities  must bridge gap to machine parameters
Machine operator
  Needs to specify non-plasma pulse procedures which need the cooperation of a number of plant systems, e.g. baking, GDC, etc.
Scheduling

## Slide 5: Stakeholder analysis and requirements
Plant system expert:
  Wants to retain ownership of his particular plant system settings (version control, different lifecycles, etc)
  wants be able to re-configure plant system on demand ( commissioning) irrespective of a pulse
  Wants to have possibility to specify constraints and dependencies of configuration values (lesson learnt from JET)
  Needs decent support tools to enable above
  Wants to be constrained as little as possible
Scheduling

## Slide 6
Scheduling
Configuration is an interplay of two CODAC systems
  PSPS
  SUP
and all plant systems
PSPS provides tools to create, edit and manage configurations
All configurations are passed to plant systems via SUP using EPICS channel access, either as part of pulse preparation and on demand if applicable
Interface to plant systems are EPICS process variables
Scope and context

## Slide 7: Scope and context
Plant system configuration captured in independent, version controlled objects
Stored centrally, but under control of plant system RO
Separation of concern between SUP and PSS
All configurations are passed to plant systems via SUP using EPICS channel access, either as part of pulse preparation and on demand if applicable
Pulse Scheduling system provides tools also to plant system RO to easily compile and manage configuration objects
via HMI
via snapshots
Scheduling

## Slide 8: Configuration Objects as atomic units
Make use of markup language based template (aka .xml schema)
  Human and machine readable
  can handle simple key-value pairs but are also flexible enough to handle complex data structures, relationships, state notations, etc.
  Can be used to describe static and dynamic configuration
  Template and instance conform to the same language
  Editor for template and instance can be identical  readily available for .xml
  Editor can customize itself automatically from template
Specialization using different templates to fulfil multiple purposes  see next slide
Allow to describe relationships and constraints between parameters internal and external to plant system
Allow for strict version control and signoff procedures
atomic blocks of which larger schedules can be composed
Derives information about variables and metadata from SDD as far as possible  need SDD support for appropriate identification of data set via configuration objects
Scheduling

## Slide 9: Template, schema, configuration object
Configuration template
Dependency template
Configuration template
Dependency template
Configuration objects are instantiated (filled) templates
Plant system specific structure
also version controlled
Internal and external constraints
Logic and/or function calls to automatically derive values
Scheduling

## Slide 10: How to build a pulse schedule? – LEGO™
Level 0: configuration objects for necessary plant systems
  Contains the configuration data which remains constant during a pulse or will change event based, e.g. two sets of configuration parameters which may depend on an event to trigger change
Level 1: PCS configuration (algorithms and architecture, not parameters)  RTF config schema
Level 2: segment information with all necessary parameters/waveforms/etc.
Level 3: metadata such as operational limits, pulse number, physics goal, audit trail etc.
Pulse schedule composed of building blocks
Scheduling

## Slide 11: Architecture concept for scheduling software
Separate HMI from underlying infrastructure
Abstraction from data sources
Support for service-based architectures to allow full re-usability in different environments
Similar to DIIRT in the EPICS world
Architecture design foreseen for 2016
Targeted support for FAT/SAT from CCS 2016a
Scheduling
G. Carcassi
Example:

## Slide 12: Functional scope
Orchestration
  Automated orchestration of plasma pulse preparation
  Execution of conditioning functions w/out plasma (GDC, baking, etc.)
  Execution of other operationally relevant procedures which can be automated (start-up, transitions to short-term maintenance, etc.)
  Manage interdependencies between functional groups and Plant Systems
    Verify relevant pre-conditions prior to attempting any action
    Control Plant Systems to reach required passive state
Timing
  Management of countdown phase and definition of pulse time scale
Configuration
  Verification, validation and propagation of machine configuration to PCS and all PS I&C
Monitoring
  Monitor system and infrastructure health, pulse schedule execution, etc.
  Verify machine state is adequate for the intended configuration, etc.
  Provide Plant-level status information
SUP & automation
Notes: 12

## Slide 13: Orchestration
SUP orchestrates activities prior to, and just after plasma pulse
  Human-in-the-loop automation
  SUP involved during pulse only for monitoring purposes
Interdependencies between functional groups and Plant Systems may have to be managed in order to orchestrate the pulse preparation phase
  Conditions in one part of the machine required prior to start of an activity in another part
SUP & automation
Notes: 13

## Slide 14: Configuration
Retrieve PCS and Plant System I&C configuration from the pulse schedule identified for execution
  Machine configuration is fully defined in the schedule by the experimenter, EiC and machine experts
Perform final engineering verification of the pulse schedule data
  Verify against operational limits ‘of the day’
    E.g. some Plant Systems may not be able to deliver full performance
  Verify or resolve dependency to machine state (and/or history)
    E.g. neutron budget, accumulated mech. stress, etc. pre-conditions or constraints
  Availability of required Plant Systems
    E.g. some required PS may not be available
Propagate configuration using appropriate interface
  Configuration to all Plant System I&C, PCS, etc.
SUP & automation
Notes: 14

## Slide 15: Monitoring
Detect faults of failure during preparation phase
  Human decision to abort or pause/recover
Verify that Plant Systems have reached required state prior to hand-over to PCS
  Monitoring and notification during pulse
  No automated action foreseen, yet informing operation about operationally relevant situation incl. in non plasma-related systems
Continuous monitoring of machine state and infrastructure health
  Extremely large scope, take a chance at detecting relevant conditions before they become issues
  Incl. availability of all expected hardware, software, infrastructure resources
Provide middle-layer service
  Elaborate Plant-level state information combining information spanning more than one Plant System I&C
  Support notification of Plant-level or context-specific alarms
SUP & automation
Notes: 15

## Slide 16: Architecture & schedule
Functional overlap with scheduling for validation  common infrastructure foreseen to allow re-useable algorithms
EPICS will allow for direct implementation of most slow monitoring functions using IOC’s and PV’s as a middlelayer service
Prototyping/phase 1 design work will begin in 2016 with releases foreseen on a yearly basis starting 2017
Support for FAT/SAT available with CCS 2016a
SUP & automation

## Slide 17: Implementation of real-time tasks
These tasks typically concern systems which contribute to real-time plasma control, e.g. diagnostics, PCS and actuator systems
  Control functions will take diagnostic measurements as input
  Procurement of I&C for diagnostic and actuator systems is in scope of various DA’s
division of responsibilities for different parts of a control cycle (measurement, algorithm, actuation) is a (major) headache  maintainability, consistency and flexibility.
CODAC is responsible to implement control functions specified by POP, but not only those. In addition:
  Integrated commissioning support
  Real-time protection
one integrated solution for implementation and development of real-time tasks for all stakeholders highly desirable
Real-time

## Slide 18: Diagnostics and plasma control: IF flow
Real-time

## Slide 19: Challenge: diagnostic integration
Don’t try to read that, but the bottom line:
Around 50 diagnostics provide around 60 measurements with a highly non-diagonal coupling matrix
IO CODAC and diagnostic will implement these functions centrally to simplify interface management & maintainability
Real-time

## Slide 20: Simplification of implementation
Diagnostic signal conditioning
  Provide toolset to DA’s to facilitate implementation of real-time tasks within plant system I&C and allow for seamless integration into distributed control  large synergy can be achieved through reusability and simplified acceptance
Derivation of diagnostic measurements
  Typically combines input from multiple diagnostics and responsibility is somewhat ambiguously defined in current IO procurement scheme
  Common infrastructure and centralization of implementation simplifies life for everyone as interfaces become internal to IO
  CODAC and diagnostics are pursuing agreement to centralize implementation (CODAC) while specification of algorithms remains within scope of the DA’s
PCS
  Implementation in scope of CODAC, specification in scope of POP
  Infrastructure requirements are superset of requirements for diagnostic measurements
IO will provide a framework to fulfil all requirements for 1-3
in time for DA to implement their diagnostic scope
Real-time

## Slide 21: Key features of a framework
Multi-platform C++ middleware
  “Simulink-type” way of describing the problem
Modular
  Clear separation between algorithms, hardware interaction and system configuration
    Change input data sources (e.g. data from archive to test algorithm) without the code even knowing
    Full access to all data inside the framework (e.g. cross-diagnostic input if needed)
    Test the code in any environment (e.g. windows PC in the office, at another fusion machine)
  Reusability and maintainability
  Simulation capability
  Configuration driven
  Integration with rapid prototyping environment (e.g. Simulink) and automated code generation
Minimize constraints due to operational environment (portability)
  Can run in the office or in a real-time environment, so any code developed can be transferred from one environment to the other without re-compilation aka. test at diagnostic algorithms at existing machine– implement at ITER with minimum hassle
Let developer focus on what he knows best and provides extensive support services
  Statistics and connection to and abstraction from external components (logging, archiving, networks etc.)
Real-time

## Slide 22: Scope of the development environment
Make use of rapid prototyping software now commonly available offering very elegant and easy ways of creating algorithms without worrying about infrastructure, e.g. Simulink
Focus on the graphical development of algorithms without low-level programming
  Support multi-machine modeling with device-independent and device-specific libraries
  Support model validation and provide appropriate analysis tools
  Support simultaneous archive of simulation setup and results
  Support easy connection of module inputs/outputs
  And finally: coupling to real-time framework to make use of automated code generation from graphical algorithm model
Real-time

## Slide 23: Objective: reduce development time/effort
Architecture and algorithm development in both diagnostics and control
  Minimize time, cost, and effort
  Maximize performance and reduce risk
Flexible & easy to use:
  for developing and prototyping PCS/diagnostics/actuator algorithms
  for constructing Plant simulations for testing
  for both open- and closed-loop simulation testing
Fast execution of "accurate enough" simulations
Archive/restore of simulation data:
  Results data: support examining/documenting test results
  Setup data: support test cases, automated test suites
  Simulation State: support reproduction of prior simulations, starting at user-selected times (special type of Results data)
Automated conversion into framework modules without need for manual coding
Real-time

## Slide 24: Simulation support: PCSSP
plant simulation may include modules for
  plasma
  actuators
  diagnostics
  Interlock
  interfaces with ext.modules
PCS simulation may include modules for
  (continuous) controllers
  Pulse Supervision Control
Event Generator(s) functionality
  to provoke events not implicitly generated by plant / PCS modules
Supervision
Control
Event
Generator
Event
Generator
PCS
Simulator
Continuous
Control
Tokamak Plant Simulator
  Project is ongoing with DINA and RAPTOR codes being integrated into PCCSP
  Public release foreseen for second half of 2015
Real-time

## Slide 25: Timeline, Outlook & Conclusion
Scope well identified for both SUP and scheduling and prototyping work in ongoing driven by FAT/SAT support for plant systems
Concept of schema-based configuration objects as atomic units of a pulse schedule fulfils all use cases
Architectural design work for both SUP and scheduling will begin in 2016 with releases foreseen on a yearly basis starting 2017
Support for FAT/SAT available with CCS 2016a for both applications
Supply of real-time infrastructure requested by diagnostics to support DA’s, implement IO internal scope and simplify interface management
Requirements for infrastructure have been identified and architecture design has been started in 2014 and will be finalized with a target date of 2016.
PCSSP is progressing well with public release foreseen this year and integration of several larger codes foreseen.
Development has slowed down compared to IAEA 2013 target as need date is pushed back due to schedule delay but is still ongoing

## Slide 26: Thank you for your attention.
Questions?